## Slide 1
Networking
Fundamentals:
Technical Report
Week 1 Assignment Analysis | DG Intern Hub

## Slide 2
Logical addressing
and path
determination
(IPv4/IPv6, ICMP).
Bitstream
transmission over
physical media like
Ethernet or Fiber.
Manages inter-host
communication and
session
synchronization.
Interface for
network services
like HTTP/S, DNS,
and SMTP.
L1 Physical
L3 Network
L5 Session
L7 Application
OSI Model: Layered Architecture
L2 Data Link
L6 Presentation
L4 Transport
Handles data
syntax, encryption
(TLS), and
compression.
Segmentation, flow
control, and error
recovery
(TCP/UDP).
Framing, MAC
addressing, and
error detection
within a local
network.

## Slide 3
Cons
Pros
Application Layer: Encapsulates
OSI Session, Presentation, and
Application layers.
Transport Layer: Direct mapping
to OSI L4; handles end-to-end
reliability.
Simpler structure
Less detailed
Practical implementation
OSI's conceptual clarity
Internet Layer: Equivalent to OSI
L3; manages routing and logical
addressing.
End-to-end reliability
OSI's theoretical foundation
Mapping the conceptual framework to
the practical protocol suite
TCP/IP vs. OSI: Architectural Comparison
Network Access: Combines OSI
L1 and L2; manages the physical
network interface.

## Slide 4
DNS
53: Hierarchical system (Root,
TLD, Authoritative) for domain-to-
IP resolution.
80/443: Stateless client-server
architecture; HTTPS uses
SSL/TLS for secure transmission.
HTTP/HTTPS
DHCP
67/68: Automated IP allocation,
subnet masking, and gateway
configuration.
FTP
20/21: Dual-port protocol for
command and data stream
management.
Application Layer Protocols

## Slide 5
IPv6
IPv4
32-bit address
IP Addressing & Subnetting Logic
Limited address space prone to
exhaustion
Address Space
Capacity
Resolves IPv4 exhaustion with massive
scale
Manual or DHCP based
SLAAC and DHCPv6
Subnetting Math: Number of subnets = 2ⁿ; Usable
hosts per subnet = 2ʰ − 2.
Requires specific subnetting math for
host allocation
Configuration and
Management
Supports Stateless Address
Autoconfiguration
RFC 1918 ranges
Global Unicast
Utilizes 10.0.0.0/8, 172.16.0.0/12, and
192.168.0.0/16
Private
Addressing
Designed for end-to-end reachability
without NAT
128-bit addressing

## Slide 6
CLI Troubleshooting: PING &
ICMP
0%
milliseconds
hop count
Packet loss
RTT
TTL
0% packet loss indicates a reachable
destination.
RTT (Round-Trip Time) measures network
latency in milliseconds.
TTL (Time To Live) values help identify the
operating system and hop count.
Connectivity verification and latency analysis using Echo Request/Reply

## Slide 7
IPCONFIG /ALL Network Data
Physical Address
48-bit MAC address for
Layer 2 identification.
DHCP Status
DNS Servers
Lease obtained/expires
timestamps and DHCP
server IP.
Primary and secondary re-
solvers configured for the
interface.

## Slide 8
CLI Troubleshooting: TRACERT
Analyze hop
output
Trigger ICMP
messages
Review hop number,
response times for 3
probes, and device
IP or Hostname.
Trace Layer 3 path
Incremental TTL
values trigger ICMP
Time Exceeded
messages from
routers.
Identify routers and
potential points of
failure along the
network path.

## Slide 9
Configure interface IP and enable it
Connectivity Validation
Router Configuration
Virtual network configuration and end-
to-end connectivity simulation
Assign static IP and default gateway
PC Configuration
Cisco Packet
Tracer:
Topology
Design
Disconnected network devices
Configuration: Static IP
192.168.1.10/24 on PC;
Default Gateway 192.168.1.1.
Router CLI: interface g0/0, ip address
192.168.1.1 255.255.255.0, no
shutdown.
Validation: Successful ICMP ping
from PC to Router interface confirms
routing.
Connected Network
Initial Network
End-to-end connectivity simulation
Ping router interface from PC

## Slide 10
Technical Learning Outcomes
Subnetting mastery
Mastery of CIDR notation
and complex subnetting
calculations.
Diagnostic interpretation
Interpretation of granular
ipconfig /all and tracert
diagnostic outputs.
Cisco configuration
Hands-on CLI configuration
and testing of Cisco
networking devices.

## Slide 11
Time-consuming
Outcomes
Systematic testing
Repeated practice
Challenges & Resolutions
Requires expertise
Cons
CIDR analysis
Pros
Potential for errors
Cable checks
Interface status
Subnetting: Resolved through repeated calculation
practice and CIDR analysis. CLI Interpretation:
Gained proficiency in reading DHCP and DNS
server details. Connectivity: Resolved through
systematic cable and interface status checks.

## Slide 12
Conclusion
Foundation for
Network Security
Integrating networking theory with practical CLI and
simulation tasks